## Slide 1
Team Members:
Arwa Hesham
Hamza Abbas
Ahmed Emad
Embedded AC Control System KH5023FTE

## Slide 2: AGENDA
Project Description
Key Components
Functionalities
Design Architecture of the Application
Software Implementation
Video Demo
SW Test Cases used vs Use cases covered
Development of Best Cost-Effective BOM
Conclusion
Q&A

## Slide 3: Project Description
Project Purpose:
                Automates room temperature regulation using an embedded system.
                Provides precise user control over ambient temperature.
Objectives:
Real-time monitoring of ambient temperature using LM35 sensor.
User interaction via keypad (Mode 1) and increment/decrement push buttons (Mode 2).
Automatic fan speed and direction control to reach the desired temperature.
Visual feedback through a LCD and LED indicators.
Data storage using EEPROM and time tracking with RTC.

## Slide 4: Key Components
Microcontroller: ATmega328P, 16 MHz system clock.
Temperature Sensor: LM35 analog sensor.
Fan Actuator: DC motor controlled via PWM for speed, GPIO for direction.
User Interface: Keypad and push buttons for mode selection and temperature input.
Display & Indicators: 16×2 LCD and LED for operational feedback.
Data Storage: EEPROM for settings, RTC module for time-based functionality.

## Slide 5: Functionalities
Continuously acquires ambient temperature and converts analog readings to Celsius.
Compares actual temperature with desired temperature to regulate fan speed and direction.
Handles user inputs with software debouncing and validation.
Updates LCD efficiently to display current and desired temperature, system mode and time .
Turns LED ON/OFF based on fan operation status.
Stores and retrieves user-defined settings from EEPROM.

## Slide 6: Design Architecture of the Application

## Slide 7: Software Implementation
Core Algorithms:
Read LM35 sensor data via ADC.
Compare real-time temperature with desired temperature.
Adjust DC motor (fan) speed and direction using PWM.
Mode switching between keypad input (Mode 1) and increment/decrement buttons (Mode 2).
User Input Handling:
Keypad scanning, push button debouncing, and validation.
Display Management:
Display all parameters on the LCD (current temprature, required temprature, time, motor(fan) status.
Alert System:
LED indicates fan operational status
.
Data Logging:
Store user settings in EEPROM; use RTC for time-based features.

## Slide 8: Video Demo

## Slide 9: SW Test Cases used vs Use cases covered
Use Case | Test Case Description | Status
Set Desired Temperature via Keypad (Mode 1) | Enter a temperature and verify that fan speed adjusts accordingly | ✅ Pass
Increment/Decrement Temperature (Mode 2) | Press buttons to adjust temperature; verify fan reacts properly | ✅ Pass
Temperature Monitoring | LM35 readings match actual ambient temperature | ✅ Pass
Fan Speed & Direction Control | PWM duty cycle changes fan speed; direction pin controls airflow | ✅ Pass
LED Indicator | LED turns ON/OFF corresponding to fan operation | ✅ Pass
LCD Display Update | LCD shows current temp, desired temp, and mode | ✅ Pass

## Slide 10: Development of Best Cost-Effective BOM
Part | Total price
Jumper Wires | 181.50
Temperature Sensor | 221.50
MotorDriver | 226.50
RTC | 291.50
EEPROM | 311.50
Keypad | 323.50
I2C LCD 2x16 Display | 468.50
L9110s | 503.5
AA Battery | 523.5
Part | Total price
Microcontroller | 120.00
Crystal Oscillator | 125.00
Voltage Regulator | 135.50
Capacitor | 125.50
LED | 131.00
Resistors | 132.50
Motor | 137.50
Push Button | 141.50
Mini Breadboard | 176.50

## Slide 11: Conclusion
The system successfully provides automated temperature control using an embedded microcontroller-based design.
Real-time temperature monitoring and accurate fan regulation were achieved through the LM35 sensor and PWM motor control.
The user interface offers reliable interaction via keypad entry and push-button adjustment modes.
LCD and LED indicators ensured clear feedback and system transparency during operation.
The modular hardware–software architecture improved maintainability, scalability, and overall system robustness.
Testing confirmed stable performance, accurate sensing, and effective response to temperature changes.

## Slide 12
Any Questions?
Thank You